# Press Release kx61-e

# Trade Press

Hagen Award for Kautex Maschinenbau

C3LS® - an alternative manufacturing method for LEV3 and PZEV capable plastic fuel tanks

As emission standards are becoming ever more stringent, tank fittings of plastic fuel tanks are increasingly relocated into the tank interior. A new manufacturing method in extrusion blow molding has now earned Kautex Maschinenbau GmbH (Bonn) the Dr. Reinold Hagen Award 2011.

For the ninth time already, the Dr. Reinold Hagen foundation (Bonn) has honored pioneering developments in blow molding engineering with its "Innovation in Blow Molding" award. This year's winner was announced on October 5, 2011 on the occasion of the "Blow Molding Engineering 2011" convention organized by the Association of German Engineers (VDI) in Baden Baden. An independent jury of members of the Blow Molding advisory board of the VDI Plastics Engineering department had selected the winner from a number of high-caliber submissions.

In plastic fuel tanks, the permeation of hydrocarbons through the wall is usually prevented by a special barrier layer as part of a 6-layer coextrusion process. However, if service openings or holes are created subsequently, the barrier layer will be destroyed. On the other hand, statutory requirements are becoming more and more demanding, for instance the US standards LEV III (Low Emission Vehicle) or PZEV (Partial Zero-Emissions Vehicle). Many efforts are thus focused on integrating the process of fitting interior tank components, such as the fuel pump, directly into the blow molding process.

As an alternative to known methods such as the various twin-sheet methods (TSBM, NGFS), the Ship-in-the-bottle (SIB) or Tank Advanced Process Technology (TAPT) processes, the experts at Kautex Maschinenbau have now developed a new method. In the so-called C3LS® blow molding process, the tubular parison is slit open in longitudinal direction at one point while it is being extruded and is unfolded. With the blow mold partly closed, components such as fuel pump, level indicator, anti-splash baffle, valves and venting conduits can now be introduced through the opening created in the parison into the interior of the pre-blown tank bladder.

Apart from lower costs of the blow mold, the new method also results in a more compact design of the machine. It can be combined with the tried and tested Kautex 6 layer coextrusion head technology and the known wall thickness control systems.

"The jury honored Kautex Maschinenbau for the C3LS method with the Dr. Reinold Hagen Award 2011 because this is a highly topical and practical innovation", commented Dr. Olaf Bruch, Head of Research and Development with the Dr. Reinold Hagen foundation.

Mr. Andreas Lichtenauer, Managing Director of Kautex Maschinenbau,  said: "We are proud to win this coveted award as it is a clear acknowledgement of the quest for innovation pursued so relentlessly by our company."

(2900 characters including spaces)

© Kautex Maschinenbau GmbH 2011 - Copy permitted, please submit 2 print copies

Reprint free, two voucher copies requested

Contact concerning the project (e.g. to be printed under the article)

Kautex Maschinenbau GmbH

Kautexstr. 54

53229 Bonn, Germany

Tel.: +49 (0) 228 489 0

Fax: +49 (0) 228 489 414

info@kautex-group.com

Editorial contact

polymediaconsult

Dr. Michael Thielen

Dammer Str. 112

41066 Mönchengladbach

Tel.: +49 (0) 2161 664864

Fax: +49 (0) 2161 631045

mt@polymediaconsult.de

The picture is enclosed as high gloss print or is available as high resolution JPG-file upon request per e-mail or can be downloaded from www.polymediaconsult.de (Press-Service) as high resolution JPG-versions. Here you will also find PDF versions of this release in different languages.

- Are you the appropriate receiver for press releases of this kind ?

- Is the address correct to which we have sent this press release ?

- Should we send press releases of this kind to a different person (too) ?

Please let us know. mt@polymediaconsult.com